Rules on Daily Auctions of Available Transmission Capacities for 2010 on the SEPS-WPS Cross-Border Transmission Profile

Organised Unilaterally by SEPS, a.s.

The bottlenecks arise on the cross-border transmission profiles1) by demand outstripping the real transmission possibilities. The process of allocating the cross-border transmission capacities of these bottlenecks is carried out through auctions.

The auction is an objective, non-discriminatory process of the cross-border transmission capacities allocation eliminating the speculative behaviour and in compliance with the requirements of Regulation of European Parliament and the Council No. 1228/2003/EC, resulting in the transmission capacity reservation on the specified cross-border profiles in a given direction. It establishes the principles of the transmission system bottlenecks management required by the safe and reliable operation of the transmission system.

Any actions and steps carried out hereunder shall have regard for the scale of data flows, implementation time conditions and data protection and security requirements implemented in electronic format.

Available transmission capacities for 2010 trading days shall be allocated to the market participants through auctions. The capacities shall be offered as unilaterally provided except for the provisions for damage prevention and those dealing with force majeure, emergency condition and emergency condition prevention issues under Slovak Republic´s generally applicable legislation.

Daily auctions of available transmission capacities on the SEPS-WPS cross-border profile shall be organised by the Auction Office, meaning SEPS, a.s. Auction Office in this case.

1. Realisation of daily auctions

Given the scale of data flows, implementation time conditions and data protection and security requirements, daily auctions shall be carried out in the Damas e-Portal - run by SEPS, a.s., at http://damas.sepsas.sk. Access to the Damas e-Portal is possible through guaranteed e-signatures validated by qualified certificates issued by an accredited certification authority. Any data exchange between the user and the Damas e-Portal via the Internet is safeguarded against reading by third parties by SSL ciphering. This e-Portal posts up any information contained in the document “Damas e-Portal Operation Rules” (hereinafter referred to as the Damas Rules) published at http://www.sepsas.sk/. In e-communications the auction participant undertakes to follow the Damas Rules and use e-forms described therein.

In case of major technical problems - e.g. an Internet widespread collapse, a collapse of all the Damas ePortal Internet connections, a Damas e-Portal collapse (servers, database or an error in Damas e-Portal applications) - a daily auction shall not be organised and this shall not be subject to any compensations. In case of major technical problems preventing it from being completed, the daily auction shall be cancelled and this shall not be subject to any compensations.

2. Requirements for Participating in the Auction Procedures

On the SEPS, a.s. side it is necessary to have a valid and effective Agreement on Electricity Transmission through Connecting Lines and Agreement on Settlement of Deviation. Participation in auctions and use of allocated capacities while respecting the 1:1 principle means that access to auctions and use of allocated capacities are only allowed for a market participant meeting any of the following conditions:

- it satisfies the conditions of both Transmission System Operators (TSOs) (SEPS, a.s. and WPS)

- it satisfies the conditions of the operator SEPS, a.s., and its exclusive partner under the 1:1 principle satisfies the conditions of the operator WPS.

Every SEPS-side party shall prove SEPS, a.s., Auction Office its WPS-side exclusive partner on the form “Announcement about exclusive partnership registration - system 1:1“ (see Annex 1 to these Rules). The confirmation of the registration shall be issued by SEPS, a.s. Auction Office. The registration shall only take place for integer calendar months and the registration application shall be delivered to SEPS, a.s., at least 5 working days prior to the 1st day of the calendar month for which the registration is required.

SEPS, a.s., shall register market participants with ensured access to SEPS, a.s., and WPS networks while respecting the 1:1 principle based on the information to be supplied by SEPS-side parties. At the request from the market participant registered SEPS, a.s. shall issue a confirmation thereof.

Damas e-Portal shall only afford access to daily auctions for an entity meeting the conditions for access to daily auctions set out above. In case that the conditions are complied with through the exclusive partner, access to daily auctions shall only be afforded to one of the entities meeting SEPS, a.s. conditions.

3. Available transmission capacities

SEPS, a.s. shall offer separately from WPS in the daily auction available capacities at the respective hours of the day, to be established especially for each direction as a difference between the total negotiable capacity of the line in a given direction established by both TSOs and the sum of the agreed transmissions of the individual market participants for a given hour, which have been agreed using the capacity allocated in the annual and/or monthly auction.

The part of the capacity allocated in the annual and/or monthly auction, which has not been used up by the users to negotiate transmission no later than 7:45 a.m. on the day preceding the realisation day, shall thus be allocated in the daily auction together with a contingent increase in the maximum value of the overall negotiable capacity arising out of the technical assessment of the network situation undertaken by SEPS, a.s. and WPS.

The available capacity offered in the daily auction shall be published in Damas e-Portal every day at 09:00 a.m. The capacity shall be published for every hour of the day, separately for WPS to SEPS and SEPS to WPS directions.

4. Transmission capacity auction request

To take part in the daily auction, the request shall be delivered over the period from the publication of capacities to 10:00 hrs. The auction participant shall make bids for auction via Damas e-Portal in such way and structure as defined by the Damas Rules.

Any request shall set out:

- auction participant,

- specification of the profile,

- specification of the transmission direction,

- trading day and trading hour which the bid concerns

- For each hour of the day the amount of the transmission capacity to be reserved in MW (natural numbers, maximal the published ATC in each hour.)

- The value of the bid in EUR/MW (max. two decimals) in each hour - it has to be equal to zero or bigger than zero.

The auction participant shall be given confirmation of the entry into Damas e-Portal of the requests. In case that the request entry is withheld, the auction participant shall be notified of the grounds therefor. Any communications with the system shall be archived and any message shall be time-flagged when going in or out Damas e-Portal. Time-flagging shall be done according to the system time displayed in Damas e-Portal´s user environment, which all data delivery deadlines are linked to.

A bid made after the deadline or failing to comply with the conditions above shall not be accepted.

5. Capacity auction procedure

All received bids for respective hour are ordered by descending bid price. In case two or more delivered bids offer the same price per MW for the auctioned capacities, the earliest will take priority (the decisive criterion is the time stamp on the bid). Bids are met in that order until a bid exceeds ATC value in sum with all previous accepted bids.

If the total amount of requested reservation of capacity is smaller than the ATC or equals the ATC, payment for congestion management procedure will amount to zero, i.e. each auction participant will receive the reserved capacity according to his bid and free of charge at the bottleneck.

If the total amount of the requested reservations of capacity exceeds the available capacity for reservation, the price for the reservation of capacities shall be determined by the bid with the lowest price offer, accepted, even in an reduced amount, by SEPS, a.s. in the allocation process of the auctioned reservation of capacities (“auction price”).

This auction price shall be paid by all auction participants receiving a reservation of capacity. All auction participants receiving a reservation of capacity shall be deemed to have purchased the reservation of capacity.

The following table, Figure 1, shows an example:

Figure 1: Daily Auctioning

In this example, the charge for auctioned daily reservation is determined at 200 EUR/MW. Bidding company "a" receives a total of 10 MW and has to pay 2000 EUR, "b" receives a total of 40 MW and has to pay 8000 EUR – second bid of the bidding company “b” is reduced.

In case all delivered bids offer the same price per MW for the auctioned capacities and the total request for the reservation of capacities is higher than the available capacity auctioned for reservation, the capacity will be allocated according to the principle “first come – first served”. The decisive criterion is the time stamp of each bid.

- Notification of the auction results

The SEPS, a.s. Auction Office shall notify each allocation party via Damas e-Portal of the following information under the Damas Rules:

- transmission capacity reservation period,

- profile and direction identification,

- the amount of the allocated transmission capacity for a given auction participant at the respective hours in MW.

The results shall be published at 10:30 hrs.

The daily auction capacity shall be allocatted on the whole profile on behalf of SEPS, a.s. A WPS-side auction participant shall ensure their required capacity separately.

7. Use of the reserved transmission capacity

An auction participant shall have acquired through the transmission capacity auction on the cross-border transmission profile SEPS, a.s. undertaking that such transmission of his is feasible while maintaining standard transmission system operation reliability levels except for force majeure, emergency condition and emergency condition prevention under the Slovak Republic´s current general legislation.

To use of the allocated capacity and agree transmission on the part of SEPS, a.s., an auction participant shall enter in Damas the agreed transmission schedules especially for every direction while respecting the 1:1 principle. The transmission schedule for the following day shall:

- entered by the market participant in Damas by D-1 1:00 p.m.

- any schedule shall contain a valid exclusive partner identification pursuant to the 1:1 principle, profile and direction,

- any schedule shall contain for every trading hour the power to be transmitted at a given hour. This value shall be a natural number and at most equal to that of the capacity allocated in the daily auction.

The schedule of the auction participant shall be compared to the value reported by the party to the Ukrainian operator. In so far as the transmission schedules do not tally in transmission value terms (MW) only, but the transmission direction tallies, less-valued transmission shall be accepted by SEPS, a.s. Unless the transmission schedules tally in the transmission direction, such unmatched schedule shall not be accepted by SEPS, a.s. - none electricity transmission shall be effected. Where the transmission schedule entered tallies with that entered with the Ukrainian operator, the transmission schedule shall be accepted.

By accepting the transmission schedule in Damas and confirming the successful entry in the system, electricity transmission shall be agreed between the auction participant and SEPS, a.s. for the day given in the request made, to the extent and under the conditions laid down in the schedule accepted. Trade shall be agreed under the number to be automatically assigned by the Damas database.

The transmission capacity rights shall be used on the “use it or lose it” principle, i.e. changes in the transmission schedule after the deadline above shall be impermissible.

8. Transfer of the reserved capacity

The rights to the capacity allocated in the daily auctions shall not be transferred.

9. Fee for the Bottleneck Management

The results of the daily capacity auctions are settled financially on half-month settlement periods (from 1st till 15th of the respective month and from 16th till end of the respective month). SEPS, a.s. will issue invoice on the 2nd working day after the respective  half-month period and will send it to the auction participant by post and a copy by fax. The auction participant shall credit the invoiced payment to SEPS, a.s. onto its account stated on the invoice. The invoice will be mature within 5 working days of its issue date.

The invoices for the auction participants from EU are obliged to contain all demanded data in accordance with the VAT law valid in Slovakia and EU. There is a customer in EU who charges and claim the VAT. For the services SEPS, a.s. issues an invoice exclusive of the VAT and informs the auction participants  about his tax liability (a treatment of “the reverse charge” is alleged). The invoices for the auction participant registered for the VAT in Slovakia will be issued including the VAT.

If the payment is not settled on the maturity date, the SEPS, a.s. Auction Office will cancel 1:1 registration of the respective auction participant. Scheduling of this 1:1 pair will be allowed next working day after the payment is credited onto the account of SEPS, a.s.

For every commenced day of delay of a payment due under this auction rules, SEPS, a.s.  is entitled to charge a default interest for the outstanding sum, with the amount of the interest being determined on a regular basis on the first working day of the calendar month at the fixed amount of 1 M EURIBOR + 3% applicable for the period of the given month. The default interest is due within 14 calendar days from the day of delivery of the invoice by fax. The invoice will be sent to the auction participant also by registered mail to the address of its seat.

All bank fees have to be paid by the auction participant. The date of payment is the date upon which the given amount is credited to the stated account of SEPS, a.s. Invoices have to be paid not later than on the maturity date stated on the invoice, free of charge and without deduction and/or offsetting (receipt of payment at the account of SEPS, a.s.).

If such a time limit expires on a public holiday, Saturday or Sunday, payment is due on the following working day.

Transmission fees such as, but not limited to, transmission fees resulting from the cross-border-tarification, including all relevant and allowable charges, will be charged independently of the payment for congestion management.

9. Dispute settlement

An auction participant and the SEPS, a.s. Auction Office shall make every effort to settle contingent arising out of, or in connection with, the daily auction procedures by conciliation. Contentious matters shall be discussed by authorised representatives of the auction participant and of the SEPS, a.s. Auction Office. A claiming Party shall be obliged to call on the other Party in writing to deal with the dispute, describing it, giving a sum, if any, up to which it appraises its claim or defining the request and producing evidence it relies its claim on. The call shall be served on the other Party in person or by registered letter.

Unless agreement is arrived at within 30 days of mailing the call to settle the dispute hereunder and under the law of the Slovak Republic, the SEPS, a.s. Auction Office or the auction participant may file a lawsuit with the competent court in the Slovak Republic.

### SEPS, a.s. Auction Office Address

SEPS, a.s Auction Office

Mlynské nivy 59/A

824 84 Bratislava 26

Slovakia

E-mail: damas@sepsas.sk

Tel:	+421 2 5069 2708

+421 2 5069 2774

+421 2 5069 2324

+421 2 5069 2473

Fax:	+421 2 5069 2393

+421 2 5069 2817

# Footnotes

1) 	A cross-border profile is a set of lines between two neighbouring transmission systems. In this case, the SEPS and WPS profile is concerned.