|  | Indicative available Transmission Capacity for cross-border exchanges of electricity |
| --- | --- |
| for the period: Year 2009 Electricity flow direction from SEPS system to system: CEPS PSE-O MAVIR WPS 700 MW 500 MW 400 MW 400 MW 1) Electricity flow direction to SEPS system from system: CEPS PSE-O MAVIR WPS 1000 MW 300 MW 400 MW 400 MW 1) Notes Values are valid for basic topology of network and typical regime state to consider criterion N-1. 1) Criterion N-1 on the profile SEPS-WPS is not fulfilled . The value is determined by SEPS, a.s. and capacities are valid for the yearly auction and are allocated through one-sided auction on SEPS, a.s. side. The value of ATC is reduced to value 0 MW during maintenance term of cross-border transmission line V440 Veľké Kapušany - Mukačevo Other trading capacities on individual profiles are determined in other stages of preparation of operation (month, day). Network bottlenecks In a case of some regime state (mainly at profile switch-off between CEPS and APG) it comes into bottlenecks on the profile SEPS - MAVIR. |