|  | Available Transmission Capacity for cross-border exchanges of electricity |
| --- | --- |
| for the period: Year 2008 Electricity flow direction from SEPS system to system: CEPS PSE-O MAVIR WPS www.e-trace.biz1) www.e-trace.biz1) 350 MW 2) 400 MW 3) Electricity flow direction to SEPS system from system: CEPS PSE-O MAVIR WPS www.e-trace.biz1) www.e-trace.biz1) 200 MW 2) 400 MW 3) Notes Values are valid for basic topology of network and typical regime state to consider criterion N-1. Criterion N-1 on the profile SEPS-WPS is not fulfilled . Other trading capacities on individual profiles are determined in other stages of preparation of operation (month, day). 1) Auction is done according to Rules published on the website www.e-trace.biz 2) On the profile with MAVIR ATC values were coordinated and agreed with MAVIR ZRt. Each of both parties allocates its part of transmission capacity with a mutual respecting of the results. For the direction from SEPS to MAVIR: NTC of the profile for year 2008: 700 MW ATC of profile allocated by SEPS, a.s.: 350 MW For the direction from MAVIR to SEPS: NTC of the profile for year 2008: 400 MW ATC of profile allocated by SEPS, a.s.: 200 MW 3) The value is determined by SEPS, a.s. and capacities are allocated through one-sided auction on SEPS, a.s. side. The value of ATC is reduced to value 0 MW during maintenance term of cross-border transmission line V440 Veľké Kapušany - Mukačevo . (preliminary term of maintenance: 3.3. - 16.3.2008, other terms will be specified within monthly preparation of operation) Network bottlenecks In a case of some regime state (mainly at line´s switch-off between CEPS and APG) it comes into bottlenecks on the profile SEPS - MAVIR. |