Time Course of Transaction Negotiations

on SEPS/CEPS Profile

valid from December 1st 2010

- The acquisition of rights for the use of the transmission capacity within pertinent directions by the by Market participants is not necessary for the provision of transmission on the profile CEPS/SEPS.

- For the negotiation of daily transmission (the period of 24 successive Trade Hours, or 23/25 hours in case of start/end of daylight-saving time), the Market participants shall submit their request not later than by 10.00 a.m. of D-2 (where D is the day of transmission).

- Market participants registered in CEPS shall submit their request in CEPS via Damas Energy (CZ) system; Market participants registered in SEPS, shall submit their request in SEPS  via Damas Energy (SK) system.

- In case of fulfilling the conditions concerning the submission of a request in compliance with Damas Energy (CZ) Rules (for Market participants registered in CEPS), or Damas Energy (SK) Rules (for Market participants registered in SEPS), the respective TSO shall accept the submitted request.

- Submitted requests for transmission have to fulfill conditions defined in the document “The User´s Guide to scheduling in CEE Region” published on www.central-ao.com, which describes rules for scheduling valid in the CEE region. Following rules are valid for requests for transmission on the SEPS/ČEPS profile:

  - Used standard ESS 3.3

  - m:n system applicable (cross-nominations)

  - Gate Closure Tine (GCT) for long-term nominations on D-2 10:00 a.m.

  - End of the correction cycle at Cut Off Time (COT) on D-2 11:00 a.m.

  - All long-term nominations on SEPS/ČEPS profile use the same CAI: LONGTERM_FREE

  - All long-term nominations on SEPS/ČEPS profile use Business Type A03 and Capacity Contract Type A06

- Within the time 10:00 of D-2, TSOs SEPS and CEPS shall perform the matching of transmission requests. If they do not match, the respective requests are refused, or reduced – with application of the rule of lower value.

- Both TSOs CEPS a SEPS shall check the technical feasibility of requests with regard to the safe and reliable operation of the transmission system. TSOs reserve the right to reduce the required matched values of transmissions in case of a jeopardized safe and reliable operation due to exceeding technical limits of TS components of this profile, or in case of a force majeure. The reduction shall be carried out in the form of proportional reduction of all matched nominations in the respective direction of the transmission; and the reduced values shall be rounded down to whole MW. Final transmission values shall be confirmed to the Market participant (User) via message sent to the user account in Damas Energy (CZ) ePortal (for Market participants registered in CEPS), and Damas Energy (SK) ePortal (for Market participants registered in SEPS) within the time by 01:00 p.m. of D-2.

- In case that within the time by 01:00 p.m. of D-2, the Market participant does not receive the message via Damas Energy (CZ) (for Market participants registered in CEPS), or Damas Energy (SK) (for Market participants registered in SEPS) on the reduction of requested transmission values within the meaning of Article 7), the transmission requests, resulting from the matching procedure within the meaning of Article 6), shall be accepted by both TSOs.

- A detailed and binding procedure for the transaction negotiation on SEPS/CEPS profile is stipulated in "Agreement on Electricity Transmission through Connecting Lines“ (for SEPS) and “Agreement concerning Accession to Trading Terms and Conditions for Cross-Border Transmission through the Transmission System in the Czech Republic in 2010” (for CEPS).