Rules for the Monthly Auction of Available Tradable Transmission Capacities for 2011 at the  SEPS-WPS Transmission Border Organized Unilaterally by SEPS, a.s.

(The Slovak version of the Rules has the priority)

Bottlenecks appear at cross-border transmission profiles because of the demand exceeding the actual transmission possibilities. The process of allocating the cross-border transmission capacities of these bottlenecks is carried out by means of auctions. Auctions at the SEPS/WPS profile are organized by SEPS, a.s. according to these Rules.

An auction is an unbiased, non-discriminatory and market-based process of allocating cross-border transmission capacities, eliminating speculative behaviour and compliant with the requirements of the Regulation of the European Parliament and Council No. 1228/2003/EC, resulting in reservations of transmission capacities at specific cross-border profiles in the given direction. It sets out principles of managing bottlenecks in the transmission system required to ensure a safe and reliable operation of the transmission system. Auction processes will be conducted in accordance with dates specified in Annex 1 to these Rules.

Any acts and actions made under these Rules must be made in writing.

The available tradable transmission capacities for the calendar months of 2011 will be allocated to market participants in the form of auctions. The capacities will be offered as unilaterally secured capacities, except planned idle times of cross-border lines and subject to provisions of loss avoidance and provisions dealing with circumstances excluding liability, emergency situations and prevention of emergency situations pursuant to the legislation generally binding in the Slovak Republic.

- Transmission Allocation Procedure

The auction of available tradable transmission capacities available for 2011 and respective calendar months of this year at the SEPS-WPS cross-border profile is held on side of SEPS, a.s. by the SEPS, a.s. Auction Office.

The offer of available tradable capacities is made depending on the direction of transmission.

Monthly auctions are carried out in the Damas Energy e-Portal - run by SEPS, a.s., at https://dae.sepsas.sk.

Access to the Damas Energy e-Portal (auction e-Portal) is possible through guaranteed e-signatures validated by qualified certificates issued by an accredited certification authority. Any data exchange between the user and the Damas Energy e-Portal via the Internet is safeguarded against reading by third parties by SSL ciphering. This e-Portal posts up any information contained in the on-line documentation of Damas Energy available at https://dae.sepsas.sk via public access. In e-communications the auction participant undertakes to follow the rules described in the on-line documentation of Damas Energy.

In case of major technical problems - e.g. an Internet widespread collapse, a collapse of all the Damas Energy e-Portal Internet connections, a Damas Energy e-Portal collapse (servers, database or an error in Damas Energy e-Portal applications) SEPS, a.s. Auction Office reserves the right to change business day regime, e.g. gate closure for bidding, time for notification of the auction results etc. All auction participants shall be informed without undue delay about actual operational situation.

These Rules for the monthly auction organized electronically in the user environment of the auction e-Portal may be replaced in case of technical problems with electronic solution identified by SEPS, a.s. Auction Office by alternative rules specified by Annex 2. Information about use of alternative monthly auction procedure according to Annex 2 will be published by 12:00 a.m. on the last working day before the final date for submitting of bids for monthly auction in terms of Annex 1 (Decesive Days for Monthly Auctions for the Year 2011). Information shall be published on the SEPS, a.s. web-page (www.sepsas.sk). Furthermore SEPS, a.s. Auction Office will notify use of alternative monthly auction procedure to all auction participants by message in auction e-Portal.

Upon submitting their auction bids for transmission capacity reservations, the auction participants undertake to pay to the SEPS, a.s. Auctions Office a fee set for Bottleneck Management whether they used the capacity reserved in the auction or not.

In order to use the capacity reserved on SEPS, a.s. side, for the transmission it is necessary to have a valid and effective Agreement on Electricity Transmission through Connecting Lines concluded with SEPS, a.s. which is conditioned by conclusion of Agreement on Settlement of Deviation with OKTE, a.s.

The reserved capacities are used upon the delivery of schedules, and their acceptance by SEPS, a.s. and approval with WPS in accordance with Article 6 thereof.

- Available Tradable Transmission Capacities

Independently on WPS, SEPS, a.s. shall offer available tradable transmission capacities at the common cross-border transmission profile in the monthly auctions for 2011. These capacities will be published on the SEPS, a.s. website as well as in the auction e-Portal in the date specified in Article 7 thereof.

- Requests to the Transmission Capacity Reservation Auction

To take part in the monthly auction, the request shall be delivered over the period from the publication of capacities to 12:00 a.m. of the Final date for submitting the bids for monthly auction in terms of Annex 1 (Decesive Days for Monthly Auctions for the Year 2011). The auction participant shall make bids for auction via Damas Energy e-Portal in such way and structure as defined by the Damas Energy Rules.

Any request shall set out:

- auction participant,

- specification of the profile,

- specification of the transmission direction,

- trading day and trading hour which the bid concerns

- For each hour of the day the amount of the transmission capacity to be reserved in MW (natural numbers, maximal the published ATC in each hour.)

- The value of the bid in EUR/MW (max. two decimals) in each hour - it has to be equal to zero or bigger than zero.

The auction participant shall be given confirmation of the entry into Damas Energy e-Portal of the requests. In case that the request entry is withheld, the auction participant shall be notified of the grounds therefor. Any communications with the system shall be archived and any message shall be time-flagged when going in or out Damas Energy e-Portal. Time-flagging shall be done according to the system time displayed in Damas Energy e-Portal´s user environment, which all data delivery deadlines are linked to.

A bid made after the deadline or failing to comply with the conditions above shall not be accepted.

- Auction Process

All received bids are ordered by descending bid price. In case two or more delivered bids offer the same price per MW for the auctioned capacities, the earliest will take priority (the decisive criterion is the time stamp on the bid). Bids are met in that order until a bid exceeds ATC value in sum with all previous accepted bids.

If the sum of the capacities required in the valid bids does not exceed the available tradable transmission capacity offered, the fee for the bottleneck management will be equal to zero, i.e. every auction participant will be given the required transmission capacity in the scope of the valid applications without the need to pay any fee for the bottleneck management.

If the sum of the capacities required in the valid bids exceeds the available tradable transmission capacity offered, the fee for the bottleneck management will be set per every 1 MW of the allocated capacity based on the lowest price from the accepted bids. The auction price set in this manner will be charged to every auction participant who will obtain a reservation of the profile transmission capacity per every 1 MW of the allocated transmission capacity reserved.

Should there be more requests with the identical bid price and the sum of these requests together with the already accepted requests exceeds the capacity offered, then these requests with the marginal price are not accepted and the remaining capacity, i.e. non-allocated transmission capacity will be offered in daily auctions.

The following table in Figure 1 is an example:

| Auction 1 Max. capacity: 200M W | SEPS ( WPS |
| --- | --- |
| Auction participant | Volume | Bid | Total |  |
|  | MW | EUR/MW | MW |  |
|  |  |  |  | Allocated |
| a | 10 | 200 | 10 | 10 MW |
| b | 20 | 50 | 30 | 20 MW |
| c | 50 | 25 | 80 | 50 MW |
| b | 20 | 22 | 100 | 20 MW |
| a | 50 | 22 | 150 | 50 MW |
| d | 30 | 20 | 180 | Exceeded 0 MW |
| e | 25 | 20 | 205 | Exceeded 0 MW |
| a | 30 | 10 | 235 | Exceeded 0 MW |
| a | 110 | 1 | 345 | Exceeded 0 MW |

Figure 1: Auction Record

In this case, the fee for bottleneck management for the given month amounted in this monthly auction to 22 EUR/MW. The “a“ auction participant will be allocated a transmission capacity of 60 MW in total and will have to pay EUR 1320 for it. The non-auctioned 50 MW will be offered in daily auctions.

The bid from “d“ and “e“ participants - 20€/MW – a marginal bid will not be accepted.

- Notice about the Auction Result

The SEPS, a.s. Auction Office will notify each successful aution participant the following information via e-Portal Damas Energy:

- profile and direction identification

- Period of reservation of the transmission capacity

- Volume of the transmission capacity reserved for the auction participant concerned in MW

- Auction price in EUR/MW for the period defined in point 2

- Fee for the bottleneck management in EUR for the period defined in point 2

- Capacity Agreement Identification (CAI) – unique identification code assigned to allocated capacity by auction e-Portal

- Use of Reserved Transmission Capacity

By reserving the transmission capacity at the cross-border transmission profile, the auction participant obtained a promise from SEPS, a.s. that his transmission can be performed up to the volume of the reserved capacity maintaining the standard level of reliability of operation of transmission systems, excepting circumstances excluding liability, emergency situations and prevention of emergency situations according to the legislation generally binding in the Slovak Republic.

Considering the fact there is not fulfiled N-1 criterion on the SEPS/WPS profile, during planned maintenance of the lines guaranteed ATC is equal O MW. Information about planned maintenance will be published on www.sepsas.sk There is no right to require compensation of fees related to allocation of ATC during planned maintenance.

The reservation of the transmission capacity at the specified transmission profile and in the specified direction becomes effective when the bottleneck management fee is paid. The rights for the reserved capacity can be transferred only when the following conditions are met:

- The auction participant shall pay the price for the bottleneck management linked with the acquirement of rights to the reserved transmission capacity use in a month, in which the rights are assigned,

- The market participant transferring rights to the reserved capacity in accordance with the Damas Energy Operation Rules transfers the capacity before 12:00 a.m. on D-3; D is business day for which the rights are transferred.

Capacity rights can be transferred for individual hours of respective business day.

The Damas Energy e-portal shall register the transfer of the rights. The transfer of the rights hereby becomes effective.

In order to use the capacity reserved on SEPS, a.s. side for the transmission it is necessary to have a valid and effective Agreement on Electricity Transmission through Connecting Lines concluded with SEPS, a.s. which is conditioned by conclusion of Agreement on Settlement of Deviation with OKTE, a.s.

The reserved capacity rights can be used following m:n principle (cross-nominations). Cross-nomination allows using of allocated capacity rights with more than one counterparty on the other side of the border. The usage of the reserved capacities is allowed only for a registered market participant meeting the conditions for using the reserved capacities and having counterparty on WPS side meeting conditions for using reserved capacities on WPS side. The capacity allocated by the SEPS, a.s. Auction Office can be used exclusively only by that market participant who meets conditions of SEPS, a.s.

The use of the reserved capacities is made upon the delivery of schedules. A binding transmission schedule for the following day must be delivered by the market participant:

- to SEPS, a.s. by 7:45 AM

Every schedule shall contain CAI code assigned to allocated capacity used by sending the nomination. In case the party and its counterparty submit not matching transmission schedules, the schedule with the lower values is determining.

It is not possible to modify the schedule after this deadline. The rights to use the reservation of the transmission capacity are applied with the "use it or lose it" principle, i.e. the transmission capacity not confirmed by a binding schedule until the specified deadline, will be offered again under daily auctions of available tradable transmission capacities to all market participants.

- Decisive Dates

- Publication of available transmission capacities -	 see Annex 1 to these Rules

- Deadline to submit applications for auctions -	 see Annex 1 to these Rules

- Publication of information about auction results -	 see Annex 1 to these Rules

- Fee for the Bottleneck Management

The following terms and conditions apply for bottleneck management arising from an auction of the available tradable capacity for calendar months of 2011:

- Notified fee for bottleneck management is due untill 5 working days following the announcement of the auction results

- The fee is the condition for obtaining rights to use the reserved transmission capacity in the respective month

- If this fee is not paid within the set date, the transmission capacity reservation will not come into effect and the auction participant looses his rights to the reserved capacity, but his obligation towards SEPS, a.s. to pay the fee doesn´t become null and void. This capacity will be offered in daily auctions of the available tradable transmission capacity for the days of respective month of 2011.

- The payment date is the day in which the amount was credited to the SEPS, a.s.’s account.

- All the bank fees are borne by the auction participant.

The SEPS, a.s. Auction Office is entitled to adjust the payment by any higher cost (such as a change or introduction of taxes, fees and similar).

- Dispute Settlement

The auction participant and the SEPS, a.s. Auction Office shall make a maximum effort to settle any potential disputes arising from the procedure of monthly auctions by conciliation. Disputable matters are discussed by representatives of the auction participant and the SEPS, a.s. Auction Office authorised to do so. The claiming party is required to call the other party in writing to settle the dispute, describing the dispute and if the claim can be valuated in monetary terms, the determining the amount this party appreciates its claim, or defining its request and presenting evidence its claim is based on. The call is delivered to the other party in person or by registered mail.

If the dispute is not settled within 30 days from the remittance of the call to settle the dispute according to these Rules and the law of the Slovak Republic, the SEPS, a.s. Auction Office or the auction participant are allowed to enter a lawsuit at the competent court in the Slovak Republic.

If the dispute is not settled within 30 days from the remittance if the call to settle the dispute and if auction participants have their registered seat outside the Slovak Republic, disputes are decided in an arbitration proceeding at the Arbitration Court by the Slovak Chamber of Commerce and Industry in accordance with these Rules, according to the law of the Slovak Republic and using the arbitration code of this Arbitration Court.

# Footnotes

A cross-border profile is a set of lines between two adjacent transmission systems. In this case, it applies to the SEPS and WPS profile.